## Slide 1: ET Project Vacuum System Challenges
C.Bradaschia, A.Pasqualetti, A.Buggiani, T.Zelenova and several other contributors
Virgo Experiment / EGO – VAC team
GW meeting, Hannover, Jun 2018

## Slide 2: Summary
Starting from the 2011 study - DS - as basis of discussion toward a preliminar design.
Vacuum apparatus of present GW detectors
Vacuum apparatus of ET – basic requirements
ET – arm tubes (technologies, bake-out issue)
ET – mirror chambers systems (‘ towers’)
ET – cryogenic pumping
ET – special issues (safety, contamination, materials, quality)
ET – budget considerations
Conclusions

## Slide 3: 2G VACUUM SYSTEM
Virgo Site, Cascina (PI)
up to ≈ 9000 m3 – 29000 m2
2 UHV arms Ø=1.2m x 3 ÷ 4 km
Large chambers at arms extremities
Cryogenic pumps
Optics and laser beam are under vacuum to avoid perturbations

## Slide 4
2G VACUUM CHAMBERS
Vacuum valves up to 1m diameter
77K cryostats to pump water vapor
Main chambers
one per core optics
Arm tubes

## Slide 5
304L plain wall (3.2 or 4 mm thick), stiffeners and bellows (Virgo and LIGO)
corrugated wall, 0.8 mm thick (GEO600)
LIGO (installation phase)
GEO600
≈ 10-9 mbar, H2 prevalent (baked).
They contain ‘only’ optical baffles and the laser beam
2G VACUUM TUBES
Credits: LIGO team
Credits: GEO team

## Slide 6
Function: house main optics and complex mechanics. Often accessed for tunings.
Ø ≥ 2m, up to 11m high, 20-30 ton.
≈ 10-8 mbar, H2O prevalent (unbaked). Divided in two (three) compartments.
Metal or double o-ring seals, single o-ring for HV compartments
2G ‘MIRROR’ CHAMBERS
Inside a mirror chamber (LIGO)
Synoptic (VIRGO)

## Slide 7: 2G VACUUM Construction
Construction schedule
... Early studies and prototypes
1994 – Virgo project official startup
1996 – Design finalization
1997 – Tube contracts setup
– Towers construction
1999 – CB towers site qualification tests
– begin of tube construction
2001 – begin of tube installation
2002 – completion of vacuum enclosures
2003 – full ITF
Vacuum and Civil installations in parallel
Construction Costs
Chart: 
| Total-Vac | TubeManuf. | LargeValves | BakingSupplies | Baffles | Towers | Pumping | TubeInt.
VIRGO CONSTRUCTION COSTS | 51630 | 10123 | 965 | 700 | 433 | 4702 | 3516 | 4525
75 M€ - Nov.2000 Council report (apparatus)
Virgo case (apparatus)

## Slide 8
ET Vacuum – 2G -> 3G
Outstanding new challenges of 3G Vacuum are:
Size
Underground realization and operation
Improved vacuum level (arms)
Cryogenics
Budget
Engineering, Logistic

## Slide 9: ET Vacuum – ‘size’
ET triangular - DS
3 x (HF+LF) 10 km arms
(+ filter cavities)
ET -L (credits GL et al. Symp.18)
1 x (HF+LF) 15 km arms
(+ filter cavities)
Virgo
3 km arms
(+ 300m FC)

## Slide 10: ET – 1/3 of the chambers (DS)
2 x 10 km HF pipes
2 x 10 km LF pipes
2 x 1 km cavities
35 Large valves
4 cryogenic + 4 ancillary towers
6 long cryotraps + 4 short cryotraps
17 towers

## Slide 11
Vacuum tubes

## Slide 12: ET – Arm tubes selected req.ts (DS)
Mechanical
Diameter: ø = 0.9m (LF) and 0.75m (HF) to be refined by optics/scattering studies and inner baffles design.
Length: 60 km L _Symp.2018
120 km DS (+ Reference Cavities, LF=10÷1 km, HF=300 m).
Joint design: welded (lip or butt type).
Bellows: maximum withstanding temperature to be studied.
Supports: needed adjustment range?
Vacuum
Leak rate: 1E-10 mbar l s-1 per module (1E-09 mbar l s-1 per 1 km section).
Pressure: UHV level E-10 mbar (H2 prevalent)
Contamination: heavy-organics ‘free’ (goal ≤ 1E-14 mbar).
Sub-sections: pseudo-valves concept to be exploited .
Lifetime
Structural aging: 30 years (undergorund corrosion effects?)
Scientific obsolescence: ultimate vacuum performances to be evaluated

## Slide 13: ET – Arms pressure requirements
Residual gas noise: statistical fluctuations of the number of molecules along the laser beam
given beam profile and gas specie
DS baseline = 1.5E-10 mbar [H2+ Σ(H2O, ...)]
margin factor ≈ 4 (> 10 on pressure)
challenging
3G Facility limits (ET+...)
Larger margin need / feasibility
HF arms only ?
DS 2011
DS 2011
Notes: Virgo tube qualifications: H2 a few E-10mbar and water CO entrambi sui 5E-12 mbar (CO da RGA o reale? Da accumulo si vede, ma chi prova sia reale?, qCO=E-16 mbar.l/s.cm2= qWater) è un upper limit.

## Slide 14: ET Arm tubes: AIR BAKE-OUT
At these pressures the prevalent gas specie is H2 , the main source is the material of the chamber ( 2G = 30000 m2). Conditioning is required to meet vacuum goals.
baking at 400°C in air involves a simple oven and reduces the walls outgassing by over a factor 100 (strongly reducing the H2 content of bulk ordinary sites).
q < 2E-14 mbar l s-1cm-2 @ 20°C
Specifications control: QC.

## Slide 15: ET - Tubes manufacturing
Different industrial processes to be examined. Fabrication includes cleaning stages, air bake-out, leak tests.... Rates > 100 m / day (i.e. 2 years per single detector).
Organization: fabrication on site.
VIRGO: assembly inside ‘tunnel’
Spiral welding (LIGO/oil industry)
Rolled sheets welded longitudinally
Workshop clean areas

## Slide 16
Arms assembly
Virgo: assembly inside tunnel
Arms realized by assembling modules 15 m to 20 m long (2G).
2G Rate = 1 to 2 modules / day (production, installation) to be increased for ET
Impact on site infrastructure design (costs)
credits GL et al. Symp. ‘18

## Slide 17: ET – Arm tubes: bake-out in situ
Bake-out considered necessary to desorb water molecules (< 1E-15 mbar l s-1cm-2). Normally to be performed just one time.
Electrical distribution, fumes and heat exhaust to be addressed (typical dissipation ~ 250 W/m @ 150°C).
Shorter sections and efficient thermal insulation will help.
Alternative ‘sound’ method for water outgas reduction?
direct Joule effect by > 1000 A DC

## Slide 18: ET – Arm tubes budget challenge
Estimate 2010 (2 large companies + 2G experience) - coarse update 2018
Vacuum tube (installed) = 95 M€ - Single detector (xylophone HF+LF) - DS topology
≈ 50% of the total vacuum cost (crude estimate)
estimated raw material incidence < 20% of the installed pipe cost. Other factors: fabrication process, installation tools and manpower, baking supplies ...

## Slide 19
Circulating ideas among the ET community: ‘’Single ø≈2m pipe’’ , “double wall pipe”, ‘’Scaled pipe’’(*) , cheap raw material alternative to 304L , arms lenght optimized ... ?
Already assumed savings = narrow ø pipes vs 2G detectors (tube and tunnels). To be confirmed along with inner baffles design (optics).
Tubes: Budget reduction thoughts
Given beam profile
Tube profile
example
Arm lenght [m]
(*) To be evaluated also vs light scattering performances

## Slide 20
Mirror chambers

## Slide 21: ET – Towers requirements
Design depends on anti-seismic suspension. Improvements of 2G (Virgo):
Cryogenic: incorporating cryostat @<10K (4 chambers / LF) 2.5G KAGRA experience
Commissioning: thermal (vacuum) recovery times !
Pumping: no permanent mechanical pumps running (turbos in the Virgo case); Cryogenics will help for ET.

## Slide 22: GW chambers requirements
Optics degradation risks
Heavy organics: materials screening and pre-baking (1E-13 mbar level AB). Specificity missing.
Cleanroom class ≈ 100 (w/out laminar flow). Control of (larger) particles on chambers walls
Electropolishing, air-baking, baking in situ before optics inserption
Dust particles a few µm size as the
cause of quartz fibers damages

## Slide 23
Cryostats (Vacuum service)

## Slide 24: 2G Cryogenics traps
Large cryogenic pumps between unbaked ‘towers’ and baked ‘tubes’
Laser beam
77K Cryostat
Consumption LN2 6 lt/hr
UHV tube 3km
HV tower
Water vapor from towers is condensed on cylindrical sections 2m long cooled by liquid nitrogen at 77K
(molecules escaped from ‘towers’ to ‘tubes’ = 3% ).

## Slide 25: ET – Cryogenics (for vacuum)
Refrigeration needs: estimated magnitude 10 W @<20K; 10 kW @77K (transfer lines and storages excluded, possibly large).
Supply via liquid cryogen or cryocoolers? Choice not driven by Vacuum needs
3G Cryogenic traps: 77K and <20K sections for WATER and AIR pumping (+ thermal shielding )
4 x [10m@77K + 1m@<20K] HF
6 x [50m@77K + 5m@<20K] LF

## Slide 26
Remarks

## Slide 27: ET – ‘CB’ area chambers
Vacuum chambers study shall progress iterating with underground engineering
aim is to save cavern and tunnel excavation with affordable complexities
2010 Concept

## Slide 28: ET – Arm tubes: pumping stations
Dedicated rooms
Spaced and fast pumps following 2G solution
DS: stations @ 500m (spares @ 250m). NEG/TSP/Ions 5000 l/s H2 (TMPs for baking).
Redundancy : operation, maintenance
Distributed pumping: an option to be explored. CERN, SAES, ...
  normally needed to push the vacuum limits
  implementation in a ‘big’ GW pipe is to be studied.
A sufficiently large tunnel (or less dense) could avoid extra-excavation .
Notes: In Virgo si ottiene circa 1E-9 (N2 eq.) unbaked, a torri isolate, staz. attive circa ogni 1000m

## Slide 29: GW Vacuum – Special issues
Apparatus safety: huge volume + inner fragile components = risks of damage.
Viewports: order of 100 viewports/ITF; dedicated policy against breaking risks
Leaks: arm tubes exposed tens of years in a humid and poorly aereated environment
Materials compatibility: compromises in designing in-vacuum equipment.
Ligo picture leaking pipe?
Risk = defect + stress x time
Credits: LIGO

## Slide 30: ET Vacuum – Conclusions
Some steps toward a 3G design
Tubes technology:
Baseline: engineering studies of manufacturing and installation along with underground design definition.
Explore alternative proposals (timeline)
Cryogenics (for vacuum): support the definition of the refrigeration technique
Pumping system: NEG option
Tower chambers: start reviewing 2G design to converge on ‘tunnel’ layout