## Slide 1: Surface distortions and optical losses
Charlotte Bond
University of Birmingham
ET meeting, Hannover,
December 2012

## Slide 2
Overview
Types of mirror distortion
Modeling real mirrors in simulations
Describing the effects of surface distortions
LG33 investigation: coupling approximation
Testing results: FFT simulations
Testing results: future experiments

## Slide 3
What are mirror surface distortions?

## Slide 4: Mirror surface distortions
The deviation of a mirror surface from an ideal surface can be divided into different categories:
  Measured deviation from perfect sphere.
  Environmental effects (thermal effects, gravity sag etc).
  Scratches and point defects.
Our aim is to model realistic mirror surfaces and understand the effect these will have on the detectors.
  Simulations for Advanced LIGO commissioning.
  Derivation of requirements for future detectors.

## Slide 5: Advanced LIGO mirror maps
Measured mirror maps representing mirrors from the Advanced LIGO project are now available (GariLynn Billingsley).
High quality polishing results in extremely low rms figure error.
The mirror maps can be used easily in simulations.
Mirror maps
The term ‘mirror map` refers to a grid of data describing an optical property over the surface of a mirror.
Different types of mirror map: phase (surface height) maps, absorption maps and reflectivity maps.
Phase map
Aperture map
Phase maps:
Surface height data
Optical center (x0,y0)
Scaling of x- and y-axis
Points defined outside the mirror
Aperture maps:
Absorption data (complete absorption outside aperture)
Optical center (x0,y0)
Scaling of x- and y-axis
aLIGO map ETM08:
central 30cm
rms = 0.52nm
aLIGO map ETM08:
central 16cm
rms = 0.17nm
Notes: Extensive work carried out to characterize surface defects of aLIGO mirrors
Result: Mirror maps which detail the surface height of the mirror and can be used in our simulations.

## Slide 6: Using mirror maps in simulations
FFT codes
input field
mirror surface
output field
Modal models
mirror map
Coupling coefficients
input field
output field
Matrix of coupling coefficients calculated from the mirror map transform the input field described by HG amplitudes into the output field described by HG amplitudes.
The effect of a mirror surface is computed by multiplying a grid of complex numbers describing the input field by grid describing a function of the mirror surface.

## Slide 7: Our approach: Modal methods FINESSE

## Slide 8: Modal models
Modal models exploit the fact that a well behaved interferometer can be well described by cavity eigenmodes.
Light fields with different spatial distortions can be described by a series expansion:
n
m
unm are HG modes in Finesse
Hermite-Gauss modes: Complete set of functions which describe beam shapes with rectangular symmetry of cavity eigenmodes.
Maxtem: Value in Finesse specifying the
number of modes to be used.
Notes: Complicated light fields can be described by a sum of modes
In theory need infinite modes, in practice can describe very complicated ilght fields with limited modes (maxtem <10)

## Slide 9: Describing effects with modes
Beam shift
small misalignments
of the beam
Beam size
small curvature
mismatch between
beam and mirror
Surface distortions
Edge effects
Order 1
HG00
HG10
Shifted HG00
LG00
LG10
Large LG00
Order 2
Simple, small effects can be described well with just one HOM.
Order 1 - 10
Order 1 - 15+
More complicated effects require more modes.

## Slide 10: Let’s look at an example using the higher order mode LG33

## Slide 11: Example: LG33 investigation
LG33 mode proposed for its potential to reduce the thermal noise of the test masses.
10 modes of order 9 which will all be resonant in the arm cavities.
LG0±9
LG1±7
LG2±5
LG3±3
LG4±1
Coupling into the order 9 modes leads to highly distorted circulating beams.
Surface distortions and modes will be different in each arm, potentially resulting in an unacceptably high contrast defect at the output.
Higher order mode degeneracy
Potential problem

## Slide 12: Coupling approximation: Zernike polynomials
Coupling coefficients from individual polynomials are calculated:
n
Solving an approximation of k we get an azimuthal condition for coupling:
Mode | m
2, 5 | 2
4, 1 | 2
1, 7 | 4
4, -1 | 4
0, 9 | 6
3, -3 | 6
2, -5 | 8
1, -7 | 10
0, -9 | 12
Zernike polynomials, Zn,m, form a complete set of orthogonal functions which describe wave fronts over a unit disc. Defined by radial index (n) and azimuthal index (m).
m required for coupling from LG33 to the other order 9 LG modes

## Slide 13: LG33 investigation: results
ITM
ETM
High finesse cavity simulated with an LG33 input beam and aLIGO map applied to ETM.
Polynomial | 2, 2 | 4, 2 | 4, 4 | other
Amplitude [nm] | 0.908 | 0.202 | 0.231 | -
Power [ppm] | 4.66 | 0.331 | 0.0431 | < 0.01
We expect LG41 and LG25 to have large amplitudes in the cavity
Mode | Power [%]
3, 3 | 88.6
4, 1 | 5.70
2, 5 | 5.02
4, -1 | 0.333
1, 7 | 0.313
other | < 0.05
Circulating field with ETM08
Pure LG33 input beam
Direct coupling from etm08 calculated using Zernike approximation.
Large presence of LG41 and LG25 in the circulating beam in Finesse model agrees with the prediction by the coupling approximation.

## Slide 14: LG33 investigation: mirror requirements
Coupling approximation is used to derive mirror requirements.
Requirement: power coupled from individual polynomials < 0.01 ppm.
For the ETM08 example:
Polynomial | 2, 2 | 4, 2 | 4, 4
Amplitude [nm] | 0.042 | 0.035 | 0.10
 | Original ETM08 | Adapted ETM08
Direct coupling into order 9 [ppm] | 6.8 | 0.043
Circulating field impurity [ppm] | 114,000 | 815
See Ludovico Carbone’s talk on ‘Higher order Laguerre-Gauss modes for future GW detectors’
[1] See Bond et al. Phys. Rev. D, 2011, 84, 102002

## Slide 15: Checking modal results against FFT: Thermal challenge by Hiro Yamamoto

## Slide 16: Thermal distortions as mirror maps
Challenge: compare results of FFT with Finesse with maps representing thermal distortions.
To represent the thermal distortions in Finesse mirror maps were created using the Hello-Vinet formula.
ETM thermal map
ETM thermal map with curvature removed

## Slide 17: Thermal distortions: comparing with FFT
Plot comparing round trip loss from Finesse and FFT models for the case of thermal distortion of the ETM.
Conclusion: the modal modal converges towards the FFT result. Good agreement is reached when modes up to order 10 - 15 are used.

## Slide 18: Future experimental investigations: comparing simulation with experiment

## Slide 19: Experimental work: using mirrors with known maps
End mirror on rail to experiment with different beam sizes.
We want to measure losses in a cavity with known surface distortions for comparison with simulations.
A range of cavity mirrors from Coastline Optics with different specifications.
Mirror maps provided before coating (Coastline Optics).
We will carry out tests using different beam spot sizes to thoroughly test the effects of different distortions and compare them with simulations using the relevant maps.
We will also carry out tests using an LG33 input beam.

## Slide 20: Mirror distortions: before and after coating
For the flat mirrors we have maps before coating (Coastline Optics) and after coating (LMA). We can analyze how the coating process effects the shape of the mirrors.
Before coating
After coating

## Slide 21: Summary
Mirror distortions and thermal effects need to be better understood to increase the sensitivity of the detectors.
We have developed the analytic and simulation tools needed to analyze these effects.
Our next step is to help characterize the mirror distortions for Advanced LIGO commissioning.
Finally these tools and experience can be used to derive mirror requirements for future detectors, such as ET.

## Slide 22: Thank you for listening

## Slide 23: Other examples
LG33 with mirror maps
Edge effects
LG33 in triangular cavities
FFT
Finesse
FFT
Finesse

## Slide 24: Finesse available as open source
Main page: http://www.gwoptics.org/finesse/
  Executable
  Documentation
  Finesse examples
  Simtools
  Links to . . .
Source code: http://kvasir.sr.bham.ac.uk/redmine/projects/finesse
  Source code
  Forum
  Bug reports

## Slide 25: LG33 investigation: frequency splitting

## Slide 26: Maxtem
Same results for different routines
Don’t need high maxtem to achieve the right result

## Slide 27: Describing effects of spatial distortions
Input Gaussian beam
Distorted output
beam
Input beam
Output beam
We are interested in how distortions affect the shape of the beam.
The coupling from one mode to another is described via coupling coefficients:
Approximation of scattering into higher order modes described by Winkler [1]
Λ the spatial wavelength, w the beam spot size and A the amplitude of the distortion.
[1] Winler et al, Light scattering described in the mode picture, 1994

## Slide 28: Coupling approximation for LG33
n = 3
n = 9
Winkler coupling adapted for incident modes other than n = 0.
Higher order HG modes show more opportunity for coupling.
Not so suitable for analysis of LG modes.
Consider 2D distortions rather than 1D to try and identify ‘bad’ shapes for order 9 modes.